## Slide 1: Module : EMBEDDED SYSTEM & HARDWARE INTERFACING
Prepared by : Muhammad Syahmi

## Slide 2
DAY 1 | DAY 2 | DAY 3
Introduction to Arduino and Robotic ESP32-Cam Introduction to sensor IR sensor Ultrasonic sensor Controlling motor Project First Robot Project: Line Follower Robot Second Robot Project: Building an Obstacle Avoidance Robot | Webserver OpenCV Interfacing - camera Project Three Robot Project : Colour Detection Robot fourth Robot Project: Object Follower Robot | Introduction to sensor Servo Project Ball sorting

## Slide 3: Single-Board Microcontroller
    Single-Board microcontrollers, or simple board controller, are microcontrollers integrated with their support component into a single printed circuit board (pcb). Example include Arduino, NodeMCU and other
      While controller board are relatively easier to embed and integrated inti other system, there are limited by capabilities of the board, and we must learn its own interface and related system(Arduino IDE, Arduino language)
    Microprocessor chip
    Analog input pins
    Digital
    input/output
    pins
    USB port
    DC Power Jack
    Miscellaneous
    (resistors , capacitors,
    wiring, reset button ,etc.)

## Slide 4: microcontroller

## Slide 5: IDE software
    Integrated Development Environment (IDE) is a software tool that provides an integrated environment for writing, editing, and developing code.
    Why we need IDE? What an IDE do?
    To get started, download thonny
    *Add board manager URL to use ESP32-cam https://dl.espressif.com/dl/package_esp32_index.json

## Slide 6: Hardware-software interface
    The process of linking software program and hardware component, such as sensor, actuator, mechanism, and machine. The program talk to these hardware component through the controller. That is why this interface is also known as controller interfacing. Also the program written here is known as the controller program
Program
Controller
hardware

## Slide 7: Why we use ESP32 cam
Processors:
CPU: Xtensa dual-core 32-bit LX6 microprocessor,
Processors:
CPU: Xtensa dual-core 32-bit LX6 microprocessor,
Wireless connectivity:
  Wi-Fi: 802.11 b/g/n
  Bluetooth: v4.2
Camera:
  2 Megapixel OV2640 sensor
  Built-in flash LED
  Support many camera sensors
Memory:
  520 KB SRAM
  4MB External PSRAM
  4MB internal flash memory
Supports microSD card
Power management:
  Internal low-dropout regulator
  Individual power domain for RTC
  5μA deep sleep current
  Wake up from GPIO interrupt, timer, ADC measurements.

## Slide 8: Esp32 cam pinout

## Slide 9
Lets program a simple code
blink

## Slide 10
How to connect esp32-cam with battery

## Slide 11
Understand how motor driver work

## Slide 12
How to connect motor with esp32-cam

## Slide 13
How to connect motor with esp32-cam
esp32-cam | Motor driver | Battery | Ir sensor | Ultrasonic sensor | servo
5V | 5V | 5V | 5V | 5V | 5V
GND | GND | GND | GND | GND | GND
PWM(GPIO12) | ENA |  |  |  | 
PWM(GPIO13) | ENB |  |  |  | 
DIR(GPIO15) | IN1 |  |  |  | 
DIR(GPIO14) | IN2 |  |  |  | 
DIR(GPIO2) | IN3 |  |  |  | 
DIR(GPIO3) | IN4 |  |  |  | 
(GPIO0) |  |  | IR1 | TRG | PIN
(GPIO16) |  |  | IR2 | ECHO | 

## Slide 14
Lets build our robot and make code:
Forward()
REVERSE()
LEFT()
RIGHT()

## Slide 15: servo
What is a servo?
A servo is a small device that can rotate or move to a specific position based on control signals.
Why we use servo?
Servos are used to precisely control the position or movement of objects in various applications such as robotics, automation, remote control systems, and model making.

## Slide 16: Interfacing : Ultrasonic sensor
VCC = 3V3
GND = GND
ECHO = 13
TRIG = 15
What is an Ultrasonic Sensor? An ultrasonic sensor is an instrument that measures the distance to an object using ultrasonic sound waves. An ultrasonic sensor uses a transducer to send and receive ultrasonic pulses that relay back information about an object's proximity.

## Slide 17
LETS MAKE DISTANCE MEASUREMENT USING ULTRASONIC SENSOR:

## Slide 18: Interfacing : IR sensor
An IR (infrared) sensor is an electronic device that detects infrared radiation emitted by objects. It works by utilizing the properties of infrared light to sense proximity or motion. When an object is present, the sensor detects the infrared radiation it emits and triggers a response or provides relevant data.

## Slide 19
Lets build black and white detection using ir sensor

## Slide 20
Project 1 : Building an Obstacle Avoidance Robot
    Obstacle Avoiding Robot is an intelligent device that can automatically sense the obstacle in front of it and avoid them by turning itself in another direction.

## Slide 21
Project 2 : Line Follower Robot
    Line Follower Robot (LFR) is a simple autonomously guided robot that follows a line drawn on the ground to either detect a dark line on a white surface or a white line on a dark.
    If both sensor did not see the dark line, move forward
    If left sensor did see the dark line, move right
    If right sensor did see the dark line, move left